## Slide 1: Vaccine cold chain and storage
Hampshire and IOW Screening & Immunisation Team, NHS England
July 2023

## Slide 2: Objectives
Identify the key principles of storing vaccines
Explain the procedures for maintaining the cold chain
Discuss the steps to take when the cold chain has not been maintained

## Slide 3: Contents
What is the cold chain
Why is the cold chain important
Vaccine storage
Audit
Cold chain incidents

## Slide 4: What is the cold chain?
Manufacture
Storage depot
Surgery/ Pharmacy/
Clinic
Vaccine session
Patient
The ‘cold chain’ is the system of transporting and storing vaccines within the recommended temperature range of 2˚C to 8˚C
To preserve potency, vaccines must be kept in a ‘cold chain’ from manufacture until delivery/administration

## Slide 5: Why is the cold chain important
Vaccines are biological substances that will, under any conditions, lose potency with time
Reduces the risk of compromising the quality, efficiency and safety of the vaccine programme, and
Vaccines are in limited supply and expensive
Use of a vaccine that has not been stored between 2-8ºC as per its licensing conditions becomes “off-label” use.
Responsibility/liability rests with immunisation provider.

## Slide 6: Storage temperature
Never let the max or min exceed 8˚C or fall below 2˚C
Strive for 5˚C
Aim to maintain vaccine fridge current temp as close as possible to 5˚C as this gives a safety margin of + or – 3˚c

## Slide 7: Vaccine Storage responsibilities
Ensuring cold chain has been maintained during transport and managing receipt of vaccines directly into refrigeration
Store promptly (in original vaccine boxes)
Checking delivery for leakage, damage and discrepancies
Rotation of stock – shortest expiry date at front
Maintaining stock information system to keep track of orders, expiry dates and running total of vaccines
Ensuring adequate supply and minimise over ordering or stockpiling
Ordering is done in time for clinics

## Slide 8: Vaccine storage continued
Dedicated vaccine fridge, no specimens, milk etc
Min and Max temp maintained between +2 and +8 °C
Min, Actual & Max temp recorded daily – 4 Rs (read, record, react, reset)
Two min/max thermometers – consider use of data logger as well
Maintain good air flow around vaccines – (do not over stock)
Appropriate size for quantity of vaccines being stored in their original packaging
Locked or kept in a locked room
Power supply secured – plug guard, switch less socket, hard wired
Do not place in direct sunlight or near heat source
Defrost/calibrate/service regularly
Ensure back up facilities are available in the event of fridge failing

## Slide 9: Validated cool boxes (carriers)
When transferring/moving vaccines for off-site use
Do:
Use validated medical grade cool box and cool packs
Monitor max/min temp while box is in use
Keep vaccines in their original packaging
Take only what you need for the session
Label vaccines removed for an external session before returning to the fridge – use these asap
Cool box should be an appropriate size for the amount of vaccine needed.
Don’t:
Freeze cool packs

## Slide 10: Audit
Every week: fridge contents should be checked at least once
Every month: vaccine stock should be audited and recorded
Every three months: audit stock and temp records
Annually: Vaccine Storage Audit Tool

## Slide 11: Risk factors
Common causes of cold chain incidents
Fridge failures include:
  Extreme room temperatures
  Over stocking
Power supply issues, planned and unplanned
Vaccines not being put away

## Slide 12: Cold chain incidents
Label and quarantine
Label and quarantine all affected vaccines in a working vaccine fridge and notify relevant personnel
Identify
Identify when the cold chain was last assured (when in –range temperature took place)
Record
Identify and keep a log of any patients who have received an affected vaccine
Contact
Contact the relevant vaccine manufacturers to ascertain the stability of the quarantined vaccines.
Inform
Contact NHS England HIOW SIT (england.hiow-sit@nhs.net) for advice and support, we will cc your ICB quality lead into correspondence. SIT will likely ask provider to complete a cold chain incident checklist if not already supplied. Do not use affected vaccines until advised by SIT.
Order
Order emergency vaccine supplies through Immform to minimise disruption to immunisation services

## Slide 13: Continued
Any vaccines considered safe for use by the manufacturer should be labelled and used in accordance with the manufacturer’s instructions. Amendment to PGDs is not necessary if the vaccine has been deemed safe (PG 21:Vaccine incident guidance: Responding to errors in vaccine storage, handling and administration (publishing.service.gov.uk))
Dispose of those vaccines considered unsuitable for use, in accordance with local policy
Complete the ‘Stock Incident Capture Form’ on Immform and amend if necessary

## Slide 14: Next steps
Reflect
Take action
Learn from the experience
Share best practice
Complete a ‘Significant Event’ form and report on LFPSE or ICB reporting system
A copy of the significant event form should be sent to the Screening and Immunisation Team

## Slide 15: Summary
Vaccines
Are biological substances that will, under any conditions, lose potency with time. This irreversible process can be accelerated if they are not kept within the recommended 2-8ºC temperature range
Are in limited supply and expensive
Storage
Use a dedicated vaccine fridge, no specimens, milk etc
Fridge should be wired into switch-less sockets to avoid them being turned off accidentally. Alternatively use a plug protector/guard
Temperature
At least two named, suitably trained people need to be responsible for ordering, receipt and care of vaccines (preferably one from the nursing team and one from management)
Don't order more vaccines than required
Do observe the four Rs - Read Record Reset React
Read the temperature at the same time every day during the working week and sign the sheet
Record it in a standard fashion and on a standard form
Reset the thermometer after each reading
Rotate stock so that those with the shortest expiry date are moved to the front of the refrigerator and used first
Act if the temperature falls outside +2 to +8 degrees
DO
Audit - contents and process regularly
Contact england.hiow-sit@nhs.net for support and advice including incidents
Use resources -Vaccine incident guidance: Responding to errors in vaccine storage, handling and administration (publishing.service.gov.uk)

## Slide 16: Resources
Vaccine incident guidance: Responding to errors in vaccine storage, handling and administration: Vaccine incident guidance: Responding to errors in vaccine storage, handling and administration (publishing.service.gov.uk)
Immunisation – GOV.UK: https://www.gov.uk/government/collections/immunisation
Patient safety reporting: (LFPSE) https://record.learn-from-patient-safety-events.nhs.uk/
Cold chain audit tool: Available from SIT Team
Screening and Immunisation Team: england.hiow-sit@nhs.net
Elearning for Health immunisation module: Immunisation - elearning for healthcare (e-lfh.org.uk)